## Slide 1: Applied Millimeter Wave Radar Vibrometry
Electrical and Computer Engineering Department, Duke University
Jessica Centers, Ph.D. candidate advised by Dr. Jeffrey Krolik
Ph.D. Final Exam
April 5th, 2023

## Slide 2: Outline
Why mmW radar vibrometry?
How can mmW radar vibrometry help vehicles communicate?
Can mmW radar vibrometry lead to novel speech analysis systems?
What are the key take aways?
-Accessible Vibrometry
-mmW Radar Vibrometry
-Contributions
-Radar Vibrometry for Connected Vehicles
-Vibrational Radar Backscatter Communication
-Modeling VRBC Return
-VRBC Processing Chain with Details and Examples
-Handling Resonant Transponding Surfaces
-Upper Bound on VRBC Data Rate
-Platform Noise
-Larynx Vibrational Analysis
-Human Speech Applications
-Summary of Work
-Future Work
-Acknowledgements

## Slide 3: Accessible Vibrometry with mmW Radars
Vibrometry historically provides accurate, stand-off vibrational measurements.
  Automotive Noise, Vibration, and Harshness (NVH) Measurements [13]
  Health Monitoring of Architectural Structures [15]
  Turbine Vibrational Analysis [11]
  Loudspeaker Quality Testing [12]
  ….
  Understanding Crab Courtship [16]
Laser Doppler vibrometers (LDVs) have
been the primary sensing solution.
  Uses interferometry to detect Doppler shifts
Millimeter wave (mmW) radars are an
accessible alternative.
  Few $100s vs $10,000s
  Smaller size, weight, and power (SWaP)
Goal: Develop mmW radar vibrometry techniques in the application spaces of wireless communication and non-acoustic speech analysis systems.
Polytec VibroGo [9]
TI IWR1443 mmW Radar Evaluation Module [25]

## Slide 4: Why Millimeter Wave (mmW) Radar Vibrometry?
Smaller wavelength ability to make out vibrations with smaller amplitudes
  Vibration power is split amongst integer multiples of the vibration’s frequency in Doppler.
Advantages of mmW:
  Smaller wavelength better angular resolution,
  Larger bandwidths better range resolution,
Semiconductor advances allow for high frequency devices to provide sufficient power for operation at desirable ranges.
where is the displacement amplitude, is Bessel function of the first kind of order , is the wavelength, and is the vibrational frequency.
Power at bulk Doppler frequency Hz is
similar to narrowband FM
millimeters
millimeters
millimeters
Notes: Before I get into the two applications considered in my dissertation, let me explain why radar’s at mmW are specifically opening up the door to this sort of work. In other words, why haven’t other radars solved these problem…

## Slide 5: Dissertation’s Contributions
Vibrational Radar Backscatter Communication (VRBC)
– Novel Communication System
  Conceived of and developed a novel wireless communication system termed Vibrational Radar Backscatter Communication (VRBC) that proves particularly beneficial when mmW radars are already present for sensing.
  Developed the signal model and processing chain for detecting, isolating, and decoding modulated vibrational signals from a VRBC transponder.
  Analyzed the trade-offs of VRBC system design choices in transponder, messaging scheme, and radar parameters.
  Provided a useful theoretical upper bound on VRBC rate.
  Performed sequence detection using the Viterbi algorithm to improve the observed rate when resonant transponding surfaces are used.
  Implemented VRBC using affordable, off-the-shelf products.
J. Centers and J. Krolik, “Vibrational Radar Backscatter Communications,” in 2021 55th Asilomar Conference on Signals, Systems, and computers, pp. 1086-1090, 2021.
J. Centers and J. Krolik, “Vibrational Radar Backscatter Communications Using Resonant Transponding Surfaces,” in 2022 IEEE 12th Sensor Array and Multi-channel Signal Processing Workshop (SAM), pp. 77-75, 2022.
J. Centers and J. Krolik, “Multi-User Methods for Vibrational Radar Backscatter Communications,” in 2023 IEEE International Conference on Acoustics, Speech, and Signal Processing, [ACCEPTED], 2023.
J. Centers and J. Krolik, “Vibrational Radar Backscatter Communications Theory and Bound,” IEEE Transactions on Radar Systems, [PENDING REVIEW], 2023.

## Slide 6: Dissertation’s Contribution
Non-Acoustic Speech Analysis Systems
– Preliminary Exploration
  Used mmW radar vibrometry to observe human larynx speech-induced vibrations and compared results to those observed with an expensive LDV.
  Explored the use of larynx mmW radar vibrometry for context-blind speaker ID.
Processing Methods for mmW Radar Vibrometry
– Impact on the Broader Field
  Veered from convention range-Doppler assumptions to better capture vibrational effects on the return.
  Implemented a system identification method for estimating a vibrating surface’s response.
  Evaluated clutter filtering effects on vibrational return and provided a solution to minimize resulting errors on the return’s phase.

## Slide 7: Radar Vibrometry for Connected Vehicles
Comms. and sensing compete for radio frequency (RF) spectrum in transportation scenarios.
  Connected Vehicle Solutions: allow vehicles to share warnings or situational information
  Automotive mmW Radars: enable advanced driver assistance systems (ADAS) like lane change assistance and blind spot detection
Aug. 2022: US Court of Appeals agrees that connected vehicles are falling short [85]
  1999: FCC gave Intelligent Transportation Systems (ITS) the 5.9 GHz band
  2019: FCC recognized that “no commercially-marketed vehicles used the 5.9 GHz band to provide vehicle safety features”
Our Approach: Allow commonplace automotive mmW radars be used to also provide communication channels rather than restrict them.
5.85
5.925
5.925
f
[GHz]
5.925
ITS band – now shared with unlicensed Wi-Fi
(as of Aug. 2022)
Remaining ITS band
24 GHz NB
24 GHz WB – phasing out
Automotive LRR band
Automotive SRR band
5.895
, r < 100 m
, r > 100 m
Federal Communications Commission (FCC) Spectrum Allocations

## Slide 8: Vibrational Radar Backscatter Communications for X2V
Vibrating license plates, traffic signs, etc. can relay messages to automotive radars that appear as micro-Doppler (phase changes primarily in slow-time).
Benefits of VRBC to other anything-to-vehicle (X2V) communication solutions:
  Zero RF emission from the message source
  Simultaneous reception from different range/angles
  Low-latency since no scheduling protocols are required
  Unaffected radar operation as the waveform is unchanged
  Minimal additional infrastructure required
  Conventional backscatter comms. at mmW requires complex, expensive retro-directive antenna arrays. [51, 52]

## Slide 9: Modeling VRBC Return Assuming FMCW Radar Waveforms
Transmitted waveform is a frequency modulated continuous wave (FMCW)
Received signal contains transponder(s), clutter, and additive white Gaussian noise (AWGN)
where
where is the TX gain/attenuation
Instantaneous Frequency
Time
where following Swerling model (power related to the radar equation)

## Slide 10: VRBC Signal Model as a Function of Vibrational Displacement
Transponder returns are modeled as flat-fading surfaces such that
Clutter is modeled as a sum of non-target point scatterers
Assuming one-transponder, the full, de-chirped signal at a given receiver element is
where
where
Notes: Transponder return assumes the transponder is primarily within a resolution bin (surface roughness is less than range resolution, orientation is radar-facing, width is less than the beamwidth, ..) This holds true for a license plate at more than a couple meters. This model also holds for retro-directive reflectors.
All ranges, velocities, and displacements are radial. For the clutter, because all points span the full arc of the main beam, we can approximate the Doppler bandwidth due to the radar platform velocity to be 2/lambda v_radar Delta cos(theta).

## Slide 11: Fast-Time vs Slow-Time Processing
# of Channels
# of Samples within a Chirp
Fast-Time
# of Chirps
Slow-Time
# of Samples within a Chirp
Fast-Time
Beamforming
# of Chirps
Slow-Time
Range Processing
FFT in Fast-Time
Range Bins
# of Chirps
Slow-Time
# of Samples
Conventional fast- and slow- time signal formatting:
If constant within a chirp, the Fourier transform in fast-time does not result exactly in a peak whose complex amplitude contains Doppler
  Consequently, use the full signal for detection.
  The approximate slow-time signal does still provide a useful phase estimation.

## Slide 12: VRBC Signal Processing Chain
Target isolation and message decoding can be completed simultaneously for different transponders detected.
Many of these processing blocks perform the necessary parameter estimations for the classic comms. problem.

## Slide 13: VRBC Data Acquisition Description
Transponder: aluminum plate excited by the Dayton DAEX25
Radar: TI IWR1443 (77 GHz, 4 GHz bandwidth)
[2]
Notes: Aluminum plate = $15
Dayton DAEX25 = $12

## Slide 14: Detecting VRBC Transponders
  indexes a range-angle bin
  indexes one of potentially many VRBC tones
  𝑙 indexes harmonics of the VRBC tone
VRBC transponder detected at off broadside
Range-Angle Intensity
Prior to VRBC Sequence
Range-Angle Intensity
During VRBC Sequence
Conventional CFAR will detect anything in range-Doppler-angle space with a significant power compared to resolution cells around it.
VRBC detection must be constrained to look for VRBC-specific Doppler content.
  Consider the power at Doppler cells at integer multiples of the Doppler frequency of the peak under test.

## Slide 15: Isolating VRBC Transponders
differs from traditional range-Doppler processing to include all fast-time samples
range isolation is now accomplished using BPF
vibrational Doppler remains captured at non-dominant, range bin-associated PRF carriers

## Slide 16: Justifying Using the Direct De-Chirped Signal for Range Processing Using Simulations
Two transponders with binary frequency shift keying (FSK) sequences are simulated.
  One (the interferer) remains at the range associated with dB SNR.
  The other begins from farther away, passes the interferer, and continues closer to the radar.
Input SNR [dB]
% Symbol Error
Input SNR [dB]
% Symbol Error
Symbol Length
2 msec
stationary interfering transponder
mmW radar
transponder
of interest
  range
  closer to the radar
  farther from the radar
Input SNR
more samples = more energy

## Slide 17: Clutter Filtering
Typically achieved with a notch filter at the clutter ridge in slow-time/Doppler.
  Requires space-time adaptive processing (STAP) for complex interference.
Recall, that a tone also likely results in significant power at the clutter ridge.
Filtering out transponder return in this manner is fine for detection, but not for displacement estimation.
assuming a known displacement signal, clutter filtering effects can be known but will likely distort phase
Shallow Clutter
Filtered Phasor
Deep Clutter
Filtered Phasor
Original Phasor

## Slide 18: Towards More Ideal Clutter Filtering
To avoid phase errors in estimating displacements, better clutter filtering is required.
Resembles narrowband FM phasor diagrams  constant modulus algorithm (CMA)? [74, 75]
  Conventional CMA requires prior knowledge of the modulus radius, ie. transponder power.
where
and
Performance function:
with
Simple gradient search provides updates

## Slide 19: Synchronizing Sequences of Unknown Displacements
Conventional cross-correlation requires knowing displacement.
Model transponding surfaces as LTI:
MSC estimates the extent to which one signal can be predicted from the other using a linear model.
  Results in a peak at all preamble frequencies at the start time
  Used a preamble chirp from
Slices at symbol frequencies will reveal decaying characteristics.

## Slide 20: Transponder Impulse Response Estimation
Using the cross-spectral system ID method [70], the impulse response of the system can be obtained:
Estimate is asymptotically unbiased assuming statistically independent additive zero-mean Gaussian noise.
Transponder Natural Freq.
Hz

## Slide 21: Summary of Processing Prior to Message Decoding
Known return can be well-modeled from transponder estimates.
  Transponder Detection 
  Synchronization 
  Impulse Response Estimation 
symbol length = 0.02 sec

## Slide 22: Modeling Symbol Data Vectors for Decoding
Symbol displacements are calculated using known excitations and the estimated impulse response
with excitation signals where
input symbol
data vectors
predicted symbol
Top Level Symbol Progression
Data vectors:
  : noise-free data vector consisting of samples of for
  : BPF AWGN
where is the clutter filter coefficient for the tap

## Slide 23: Maximum Likelihood Detection
Let denote when the noise-free data vector
is derived from being the symbol.
These results aren’t great… because the transponder’s impulse response demonstrates extreme resonance.
  [Recall from my Prelim] Using similar and a less resonant surface (loudspeaker), single symbol ML gave near perfect detection at kbits rates though only at short ranges.
Rate bps
Calculating Rate
Detected Symbol,
0.96 | 0.04 | 0.00 | 0.00
0.03 | 0.31 | 0.03 | 0.63
0.04 | 0 | 0.75 | 0.21
0.10 | 0 | 0.16 | 0.74
True Symbol

## Slide 24: Handling Resonant Transponding Surfaces
Resonant surfaces lead to larger displacements but also ISI.
To use small , we must utilize sequence detection and/or coding constraints
  Model all possible symbol interval displacements due to ISI or coding constraints.
    Can require defining a negligible amount of ISI for modeling
  Describe the displacement sequence as a Markov model.
    States: defined by ISI
    Transitions: defined by a new symbol occurrence
    Transition Matrix: dependent on ISI and coding constraints
  Use the Viterbi algorithm to detect the most likely sequence.
Rate bps
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0.07 | 0.93 | 0
0.05 | 0.23 | 0.14 | 0.59
Detected Symbol
True Symbol

## Slide 25: How Resonant means Sequence Detection is Worthwhile?
Consider two transponders with impulse responses that only vary in decay factor.
  , msec, number of symbol intervals required to decay before negligible per symbol , no-consecutive symbols coding constraint

## Slide 26: An Upper Bound on VRBC Rate
Mutual Information Rate:
Data Processing Inequality:
Because
-ary upper bound on rate:
Using a lower bound for the expected value of a log-sum[72, 73]:
where is the set of displacements dependent on (symbol) and (state/ISI)
where
and
:
condition probabilities are intricate if symbol data vectors aren’t orthogonal
no analytical solution for the differential entropy of a homoscedastic (same covariance) complex Gaussian mixture
If high SNRs lead to
Notes: The actual rate calculation becomes complex to solve directly, as non-orthogonal symbols lead to complex conditional probabilities.
Can’t calculate the differential entropy of y_q exactly because it is a complex, homoscedastic Gaussian mixture (a long standing problem).

## Slide 27: Anticipated Vehicle Noise
Accelerometer ( Hz) data collection on hybrid Kia Sportage
Noise mitigation methods like that in [78] are used. (See dissertation and/or back-up slides).
Takeaways
Most vehicle noise is Hz.
  Technical literature agrees and claims vibrations mm amplitude. [76, 77]
Noise at multiple locations on a vehicle is correlated.
  One can be used to mitigate vibrational effects at the other.
Gas mode generates additional tonal noise inversely related to speed.
Accelerating from 40-60 mph
Accelerating from 40-60 mph

## Slide 28: How can mmW Radar Vibrometry help Vehicles Communicate?
Existing X2V[23]
VRBC
Range
Max
m
dependent on transponder RCS
Data
Rates
kbps
Number of
Channels
dependent on
spatial resolution
Comm.
Latency
ms
No handshaking technically needed
improvements expected with better coding/transponder design
warning
Conclusion
In places where mmW sensing is already used like in vehicles, VRBC serves as an affordable, scalable, and low latency communication solution that requires no additional RF spectrum usage.
Required
Add-Ons
RF transceivers
Vibrating transponder
RF
Spectrum
MHz
No additional

## Slide 29: What are the Key Take Aways?
Novel Communication System – Vibrational Radar Backscatter Communication
Potential Impact
affordable, scalable, and low-latency communication system that requires no additional RF spectrum when mmW sensing is already present like in connected vehicles
Description of Work
1. conceived of a new backscatter comms. system that observes modulated surface vibrations from a transponder
2. developed a comprehensive signal model and processing chain to detect, isolate, and decode VRBC transponders
3. simulated and implemented VRBC to demonstrate practicality and provide initial solutions to application-motivated challenges
Key Results
theoretical and experimental proof of system and signal processing chain capabilities
demonstrated bps performance at meters and justified kbps performance at longer ranges through simulations
significant rate improvement using application-motivated methods like sequence detection for resonant transponding surfaces

## Slide 30: Future Work
Vibrational Radar Backscatter Communication
Iterative joint transponder and messaging scheme optimization
  Improved retro-directivity
  Increased number of desirable signal symbols (tenths of millimeter vibrational displacement, orthogonal data vectors, minimal interference, … )
  Minimizing acoustic noise
  Considering non-FSK messaging schemes
Implementation of vibrational noise canceling methods
mmW Vibrometry
Refined clutter filtering methods
  Improved minimization of negative phase effects during clutter filtering
  Increase robustness in cases of platform bulk movements
  Evaluate allowable mmW radar phase noise for successful phase estimation

## Slide 31: Acknowledgements
Advisor:
Dr. Jeffrey Krolik
Committee:
Dr. Loren Nolte, Dr. Robert Calderbank, Dr. Stacy Tantum, and Dr. Donald Bliss
Current Lab Members:
Dr. Michael Martinez, Shannon Pinnell, Elliot Mueller, and Dr. Granger Hickman
Previous Lab Members:
Dr. Anil Ganti and Dr. Andrew Young
Family and Friends
Especially my parents Terry and Jeannie Bilskie and my husband Aaron Centers

## Slide 32: Questions?

## Slide 33: Radar Vibrometry for Non-Acoustic Speech Analysis
Motivated by its relation to vital signs monitoring [33-36], mmW radar vibrometry captures throat vibrations to capture speech generation information.
Our Approach: Evaluate the mmW radar’s ability to capture larynx speech-induced vibrations and consider its use in speech-based applications.

## Slide 34: mmW Radar vs LDV Larynx Vibration Measurements
Motivated by its relation to vital signs monitoring, mmW radar vibrometry captures throat vibrations to capture speech generation information.
Conventional delay-and-sum beamformer.
Consists of a fast-time DFT and capturing the complex
amplitude across a range bin.
Uses standard notch filtering in slow-time.
Adaptive line enhancer (ALE) using recursive least squares (RLS) with taps and a delay of .
Short-time Fourier Transform (STFT) with msec window length with Taylor window and overlap.
1
2
3
4
5
ALE
Recall that vibrometry data without phase estimation is the Bessel function result.
Vibrometry appears to be approximately LPF acoustic data.

## Slide 35: Biometric Identification with Vibrometry-Like Data
Inspired by [44-46], our speaker ID system was
Mel scale features measure subjective pitch according to human ear’s hearing ability.
  STFT in Mel scale using Python’s Librosa library, length filter bank, window length of msec, overlap
Convolutional layer with kernel and stride
Max pool with kernel
Convolutional layer with kernel and stride
Convolutional layer with kernel and stride
Multi-task learning using other targets in the TIMIT database.
1
2
3
4
5
6
7
8
Due to scarcity of mmW vibrometry data, LPF TIMIT [43] acoustic data was first used.

## Slide 36: Speech Recognition vs Speaker ID for LPF Audio
Automatic speech recognition (ASR) requires multiple observations of different people speaking the same words.
  TIMIT database consists every person speaking ten phonetically rich sentences.
Adopted Google Speech Recognition [48] yet recognized as a lower bound on performance as it was trained on non-filtered acoustic data.
ASR requires first harmonic to recognize speech perhaps.
Speaker ID requires less of the high harmonics of speech to perform well.

## Slide 37: Can mmW Radar Vibrometry Lead to Novel Speech Analysis Systems?
If LPF audio with ca cutoff of kHz does equation well to mmW vibrometry data, speaker ID systems could be made more contextually private.
However, further work is required to justify
  mmW radar vibrometry data set of larynx vibrations for multiple speakers saying multiple word utterances
  an ASR trainable on non-acoustic data
unobtainable

## Slide 38: What are the Key Take Aways?
Preliminary Analysis of Non-Acoustic Speech Systems – Context-Blind Speaker ID
Potential Impact
mmW vibrometry could provide a data source related to human speech generation to offer contextually private biometric identification
Description of Work
1. used mmW radar larynx vibrometry data to generate speech spectrograms similar to those often generated from acoustic data for speech analysis systems
2. evaluated the performance of different variants of data in both a speaker ID and speech recognition system
Key Results
less than dB of SNR depreciation for the first two harmonic of speech when using mmW radar vibrometry vs LDV
greater than better performance in speaker ID than speech recognition for LPF audio data that resembles mmW radar vibrometry
Future Work
Content-Blind Speaker ID
mmW radar vibrometry data set creation for human larynx vibrations during speech generation
Thorough speaker ID vs ASR performance analysis using vibrometry-trained models

## Slide 39: Bibliography

## Slide 40: Bibliography

## Slide 41: Bibliography

## Slide 42: Bibliography

## Slide 43: Bibliography

## Slide 44: Bessel Function Result for Vibrational Power
Slow-time signal at a particular fast-time range bin for a vibrating target
Plug in a tonal vibration and assume no bulk movement without loss of generality
Take its Fourier transform

## Slide 45: Swerling Model for Radar Return Gain/Attenuation Terms
Gain/Attenuation terms are complex Gaussian with a uniformly random phase and variance related to the radar equation
for
  , with
TI IWR1443 gains and losses:
  , , , noise figure,

## Slide 46: Transponder Design Considerations
Cost, size, and power: relative to the application of interest
Noise pollution: displacing surfaces leads to sound unless vacuum sealed to limit energy losses to material loss rather than acoustic radiation
Reflectivity:
  SNR , ,
  For a flat aluminum plate with and reflectivity ,
  SNRs of dB equate to distances of meters.
Ability to be controlled exactly: to avoid ISI and achieve closer to orthogonal data vectors
Provides ample displacement: resonant surfaces  larger displacement
more symbols with larger displacement  higher rates
ratio of TX power incident upon object
ratio of power reflected back
losses due to the system and atmosphere
effective aperture size of antenna(s)

## Slide 47: A Look at Other Solutions in Connected Vehicles
  Vehicle-to-vehicle (V2V) Communication
    Dedicated Short Range Communication (DSRC)
    Cellular Vehicle-to-Anything (C-V2X)
  Cooperative Sensing
    Uses spectrum sensing to reactively avoid same-band operation
  Joint Radar-Communication (JRC)
    Modulating radar waveforms to contain a communication message
  Joint Communication-Radar (JCR)
    Using a communication signal with good ambiguity function for sensing
  Unified Codesign
Codesign
Performance
Tradeoffs
Between Systems
Sharing Spectrum
Cooperation
Coexistence/
Cohabitation

## Slide 48: Why Conventional Backscatter Comm. at mmW isn’t Practical
Traditional backscatter communications modulates via transponder impedance.
Challenges of mmW Backscatter Communication :
  Path loss at higher frequencies requires mmW RFID to use complex, expensive antenna designs to return sufficiently strong signals
12 ``
24 GHz strip patch array
0.9 GHz LoRa ~$0.2
TI 77 GHz automotive radar ~$25
Notes: LoRa (long range) backscatter comms: reaching km distances, has been considered for V2X
microstrip patch antenna array: additively manufactured with inkjet printing using silver nanoparticle inks on a flexible liquid-crystal polymer substrate making it “low cost”, gigabit-data-rate at 24 GHz

## Slide 49: Narrowband Frequency Modulated (FM) Phasors
Assume message signal,
The frequency of FM signal,
The phase is therefore,
Full signal becomes,
Narrowband FM means that remains small… much less than .
  Assume and

## Slide 50: Modifier CMA for Clutter Filtering
Performance function looks to minimize the variance of the amplitude,
Allows a translation around a circle of magnitude to negate difference in bulk angle of the clutter versus transponder, where
Allows the amplitude to adaptively adjust to negate remaining clutter effects and allow for some changes in transponder power over time,
Use previous samples to estimate expected values.
Using gradient descent both adaptive variables are updated via

## Slide 51: Modifier CMA for Clutter Filtering, cont.
Let
where and
where and

## Slide 52: Putting VRBC Return into a Markov Model
Consider three FSK symbol example
Symbol intervals required to decay out to “negligible”
  Symbol 1 = 2
  Symbol 2 = 1
  Symbol 3 = 1
Coding constraint is no consecutive symbols.

## Slide 53: Why VRBC Benefits from Orthogonal Noise-Free Data Vectors
Probability of misclassifying one symbol, , for another, , is
where
If , numerator contains term
for  term is maximized if (orthogonal)
for  term is

## Slide 54: Proving the Lower Bound on the Expected Value of a Log-Sum

## Slide 55: Mitigating Vehicle Noise
Radar Platform Noise Mitigation[78]
Estimate platform noise using slow-time signal from clutter points.
Cancel clutter at all beam-range combinations of interest.
Transponder Platform Noise Mitigation
Estimate platform noise using slow-time signal from target platform points w/o transponder
Use platform noise estimate in data vector model.
for

## Slide 56: Texas Instruments IWR1443 mmW Radar